## Slide 1
RESISTANCE OF A CONDUCTOR
1
Resistance
of a Conductor
Senior High Physics · Electric Circuits

## Slide 2
RESISTANCE OF A CONDUCTOR
2
OPENING QUESTION
Why are these wires so different?
Household wiring: every gauge carries a different maximum current
High-voltage lines: thick, bare aluminium — why?
Same metal, same electricity — yet thickness, length and material all matter. By the end of this lesson you will be able to say exactly how much they matter.

## Slide 3
RESISTANCE OF A CONDUCTOR
3
CONTEXT
Sometimes resistance is the whole point
Every conductor resists
Wires, filaments, even your body — anything that carries current opposes it to some degree.
Resistors are deliberate
Manufactured components that provide a precise, reliable amount of resistance.
Why we need them
They set currents and divide voltages — the quiet workhorses of every circuit.
Fixed, variable, thermal, light-dependent — a family portrait of resistors

## Slide 4
RESISTANCE OF A CONDUCTOR
4
THE MICROSCOPIC PICTURE
Where does resistance come from?
Inside a metal, free electrons drift through a lattice of vibrating positive ions.
Each collision with an ion disturbs the drift — the accumulated effect is what we call resistance.
Drifting electrons scatter off lattice ions
Water analogy: an obstructed pipe needs more pressure for the same flow

## Slide 5
RESISTANCE OF A CONDUCTOR
5
DEFINITION
Putting a number on it
unit: ohm — 1 Ω = 1 V/A
A ratio at one operating point
R compares the voltage across a conductor with the current through it — measured together, at the same moment.
A property of the conductor
R is set by the conductor itself — its material, its dimensions, its temperature — not by the circuit you put it in.
Universal
R = U/I defines resistance for every element — linear or not. No assumptions required.

## Slide 6
RESISTANCE OF A CONDUCTOR
6
LAW
Ohm's law — and its limits
current is proportional to voltage — for some conductors, at steady temperature
✓ WHERE IT HOLDS
Metallic conductors
Electrolyte solutions
✗ WHERE IT FAILS
Gas discharge tubes
Semiconductor devices
Motors, electrolytic cells
Keep the two ideas apart: R = U/I defines resistance — always. Ohm's law claims I grows in proportion to U — a special property of some materials, not a definition.

## Slide 7
RESISTANCE OF A CONDUCTOR
7
I–U CHARACTERISTICS
Reading resistance from a graph
U–I graph: slope = R. The steeper line (A) has the larger resistance.
I–U graph: slope = 1/R. The steeper line (B) has the smaller resistance.
The same two conductors — opposite-looking pictures. Check the axes before you compare slopes.

## Slide 8
RESISTANCE OF A CONDUCTOR
8
BEYOND THE STRAIGHT LINE
Non-ohmic elements
Filament lamp. Current heats the filament; R rises, the curve bends toward the U axis.
Semiconductor diode. Resistance collapses as U rises; the curve bends toward the I axis.
R = U/I still gives the resistance at every point of these curves — what is lost is only the proportionality.

## Slide 9
RESISTANCE OF A CONDUCTOR
9
QUICK CHECK
The graph shows I against U for a conductor
Which statements are correct? Choose all that apply.
A
The element is non-linear, so R = U/I cannot be used to find its resistance
✓
B
At U = 5 V its resistance is about 5 Ω
C
Its resistance increases as the voltage rises
✓
D
Its resistance decreases as the voltage rises
ANSWER B · D Read R = U/I at each point: 5 V / 1.0 A = 5 Ω, but 10 V / 2.5 A = 4 Ω — the ratio is falling. The definition works fine on a curve; only Ohm's law is off-limits.

## Slide 10
RESISTANCE OF A CONDUCTOR
10
EXPERIMENT
What determines the resistance of a wire?
01
Length
02
Cross-section
03
Material
04
Temperature
Four suspects — so we change one at a time and hold the rest fixed: the control-variables method.

## Slide 11
RESISTANCE OF A CONDUCTOR
11
EXPERIMENT · DESIGN
One circuit, three fair comparisons
Conductors a–d in series — a voltmeter across each
a vs b
only the length differs
a vs c
only the cross-section differs
a vs d
only the material differs
In series the current is the same everywhere, so U = IR makes each voltmeter reading directly proportional to that conductor's resistance.

## Slide 12
RESISTANCE OF A CONDUCTOR
12
EXPERIMENT · RESULT
The resistance law
ρ resistivity (Ω·m) — set by the material
L length S cross-sectional area
RESISTIVITY AT 20 °C
Silver
1.6 × 10-8 Ω·m
Copper
1.7 × 10-8 Ω·m
Aluminium
2.9 × 10-8 Ω·m
Tungsten
5.3 × 10-8 Ω·m
Nichrome (alloy)
≈ 110 × 10-8 Ω·m
Double the length — double the resistance. Double the cross-section — halve it. The alloy stands a hundred times higher: that is why heating elements are nichrome, not copper.

## Slide 13
RESISTANCE OF A CONDUCTOR
13
GOING FURTHER
Resistivity moves with temperature
Metals
ρ rises steadily with T — the basis of resistance thermometers
Semiconductors
ρ falls sharply as T rises — thermistors exploit this
Superconductors
below a critical temperature, resistivity vanishes entirely
Alloys such as manganin barely move with temperature — exactly what you want in a standard resistor.

## Slide 14
RESISTANCE OF A CONDUCTOR
14
WORKED EXAMPLE 1
Resistance from a characteristic curve
Solid lines: the I–U characteristics of resistors a and b. Dashed line c is the tangent to b at U = 1 V, drawn parallel to a. Which statements are correct?
A
At U = 1 V, the resistance of b is 5 Ω
B
At U = 1 V, a and b have equal resistance
✓
C
The resistance of b rises as U rises
✓
D
At U = 3 V, a and b have equal resistance
ANSWER C · D Resistance is U/I at the point — never the slope of tangent c. For b it rises from 1 V/0.4 A = 2.5 Ω to 3 V/0.6 A = 5 Ω, matching a there — and a stays at 5 Ω throughout.

## Slide 15
RESISTANCE OF A CONDUCTOR
15
WORKED EXAMPLE 2
Testing the factors fairly
In the series circuit from our experiment, b differs from a only in length, c only in cross-section, d only in material. Which statement is correct?
A
Without an ammeter, no quantitative study is possible
✓
B
a vs b: the longer conductor gives the larger voltmeter reading
C
a vs c: the thicker conductor gives the larger reading
D
a vs d: a larger reading means the better-conducting material
ANSWER B Same current everywhere, so U = IR ranks the resistances. Longer → larger R → larger reading (B). Thicker means smaller R (C ✗); a larger reading marks the worse conductor (D ✗); and the reading ratios already give the quantitative law (A ✗).

## Slide 16
RESISTANCE OF A CONDUCTOR
16
WORKED EXAMPLE 3
Thinking straight about resistivity
Which statement about the resistivity of materials is correct?
A
Cut a wire into three equal lengths — each piece has a third of the resistivity
B
Every material's resistivity rises with temperature
✓
C
An alloy's resistivity exceeds that of the pure metals composing it
D
The larger the resistivity, the more a conductor opposes current
KEEP APART
ρ belongs to the material (and its temperature).
R belongs to the object: geometry included, via R = ρL/S.
ANSWER C Resistivity never depends on shape (A ✗). Semiconductors fall with temperature (B ✗). Opposition to current is R, which geometry also sets (D ✗). Alloys do exceed their constituent metals (C ✓).

## Slide 17
RESISTANCE OF A CONDUCTOR
17
WORKED EXAMPLE 4
One block, two resistances
A copper block has edges a > b > c. Current can be sent lengthwise (along edge a, as shown by the left arrow) or down through the thickness (edge c, top arrow). Find the ratio of the two resistances, R1 : R2.
A
1 : 1
✓
B
a² : c²
C
a² : b²
D
b² : c²
ANSWER B Same material, same block — different geometry, different resistance.

## Slide 18
RESISTANCE OF A CONDUCTOR
18
SUMMARY
What to take away
01
Definition
R = U/I — any conductor, any operating point. A ratio, never a tangent slope.
02
Ohm's law
I = U/R with R constant — a straight-line I–U graph. Metals and electrolytes only.
03
Resistance law
R = ρL/S — longer means more, thicker means less, material sets the scale.
04
Resistivity
A material property that moves with temperature: up for metals, down for thermistors, zero below the critical temperature of a superconductor.